## Slide 1: Overvoltage protection
Syed Mortuza Hasan
1606108
Mehedi Hasan Emon
1606113
Tanvir Anjum
1606115
Minhajur Rahman
1606126
Submitted by – Group B2.14

## Slide 2: Outline
Summary
Background
Methods
Simulation
PCB layout and 3d rendering
Future Outlook
Conclusion
This Photo by Unknown author is licensed under CC BY-SA.

## Slide 3: Summary
An STM32F103C6 based Digital Overvoltage Protection Circuit for Industrial Load is simulated Using Proteus® Software.

## Slide 4: Background
Vaarious external and internal phenomena cause a power supply voltage to overflow. Overvoltage in power system can cause serious harm to load material or cause overheating. In extreme cases, overvoltage may melt electric cables, cause electric/ electronic devices to malfunction and even cause fire hazard.

## Slide 5: Methods
Power Supply
Dual winding Transformer
Microcontroller Protection Circuit
Voltage Sensing Circuit
Microcontroller
Load
Relay​
Relay​

## Slide 6: Methods
We used an step down dual secondary winding transformer to bring down the line voltage to a measurable quantity.
The Voltage sensing circuit performs full-wave rectification to convert the voltage to DC and feeds it to the microcontroller for sensing
The microcontroller protection circuit senses the line voltage and controls the flow from Voltage sensing circuit to microcontroller in order to protect the microcontroller from malfunction
The microcontroller precisely senses the voltage and controls the connection between load and supply line.
The line voltage is displayed through three seven segment displays

## Slide 7
Coding: Introduction
Compiler:
STM32CubeIDE
Language:
C – programming language
Microprocessor:
STM32F103C6

## Slide 8
Coding: Clock Configuration
Clock Selected:
High Speed External (HSE)
Clock source:
Crystal/Ceramic Resonator
Logic voltage:
3.3V

## Slide 9
STM32 (Pinout)
PA1: takes an analog input between 0 and 3.3V for voltage sensing
PA0: sends the controlling logic to the load-relay controlling circuit, output type: no pushup-no pulldown
PA9: USART receiving pin
PA10: USART transmission pin
PB0-PB11: outputs the control word to the three 7 segment display, output type: pull down

## Slide 10
Coding:
while (1)​
{​
HAL_ADC_Start(&hadc1);​
HAL_ADC_PollForConversion(&hadc1, HAL_MAX_DELAY);​
raw = HAL_ADC_GetValue(&hadc1);​
temp = temp + raw;​
i = i + 1;​
if (i==10){​
x = temp/10;​
temp = 0;​
i=0;​
voltage = (x-1491)/5.6409 + 360;​
sprintf(msg, "%hu\r\n", voltage);​
HAL_UART_Transmit(&huart1, (uint8_t*)msg,strlen(msg), HAL_MAX_DELAY);​
}​
​
Description:
Raw voltage information is read through ADC using polling method​
The raw values are averaged over a period​
A linear relationship was established using two data points of raw data and voltage​
Actual voltage is measured using the relationship​
The value of the voltage is sent to virtual terminal for debugging​

## Slide 11
Coding:
a = floor(voltage/100);
b = floor(voltage/10);
b= b%10;
b = b<<4;
c = voltage%10;
c = c<<8;
GPIOB->ODR = a|b|c;
if (raw<60)
GPIOB->ODR = 0;
HAL_Delay(1);
if((voltage>466)||(raw<60))
{
HAL_GPIO_WritePin(GPIOA, GPIO_PIN_0, 0);
}
else
{
HAL_GPIO_WritePin(GPIOA, GPIO_PIN_0, 1);
}
}
}
Descriptions:
Since our three BCD 7 segment displays are connected with pins PB0-11, a 12-bit word is generated using four bits for each unit, tenth and hundredth digit
The 12-bit word is then sent to the Output Data Register of the Port B
If the measured voltage is greater than 6% of rated voltage of 440V for industrial usage, the load connecting relay is energized through mosfet
Otherwis the relay is de-enegized

## Slide 12: Simulation (Normal Operation)

## Slide 13: Simulation (Overvoltage)

## Slide 14: Simulation (Overvoltage)

## Slide 15: PCB Layout
Figure: PCB Layout
Software Used:
Proteus
Dual Layers. Blue and Red.

## Slide 16: 3d rendering
Figure: 3D Rendering
Software Used: Proteus

## Slide 17: Future Outlook
1.Implement in real life with hardware
2.Printing the PCB for practical usage
3.Undervoltage Protection
4.Unstable Frequency Protection

## Slide 18: Conclusion
The number of expensive electronic devices in private households has risen sharply in the last few years. In addition, electric appliances are becoming ever smaller and more powerful; however, they thus also react more sensitively to over voltages.
The subsequent financial damage and hassle is great when expensive electric appliances such as televisions, computers and food processors are damaged by lightning strikes and over voltages. To prevent these over voltages, overvoltage protection can reduce occurring voltage peaks to a level that is not dangerous for the terminal device.

## Slide 19: Additional Slides

## Slide 20: References
https://pdf1.alldatasheet.com/datasheet-pdf/view/201588/STMICROELECTRONICS/STM32F103C6.html
https://www.alldatasheet.com/view.jsp?Searchword=Irf540%20datasheet&gclid=CjwKCAjwgISIBhBfEiwALE19Se-YWNmCKHELvi1W34DGLMwYtGmy9618Dk2r0D5a4m65V_mQ0gBAUBoCfZcQAvD_BwE&fbclid=IwAR2RBxTMbDqrJpRa_oAzzf4MzhKFN8KeZ_L7IzePPgOcvZXpNRRWTl_gWxg
https://www.alldatasheet.com/view.jsp?Searchword=Lm339%20datasheet&gclid=CjwKCAjwgISIBhBfEiwALE19SWUDzAa8ohoZaRpWowEGKEHUA3Z_6453KZUUkh0k_80SxKZzoUhi-RoC_l0QAvD_BwE&fbclid=IwAR3-yF5OXz1ZiI2tDoUphib6ZT3vgpngwWi8zfFAm24umYYv2bjkQbFsP3s

## Slide 21: Bill of Materials
1x STM32F103C6
2x 5V Relay
2x LM339
3x BCD 7 segment display
1x Dual secondary winding Transformer
2x IRF540 MOSFET
1x Full bridge rectifier
1x diode
1x 7805 IC
5 x10k, 1x 52k,1x 100k resistors
2x 100k variable resistors
1x 10uF, 1x 100uF, 1x 1mF capacitors
1x 1mH Inductor
Wires

## Slide 22: Detailed Methods
Software used:
Proteus 8 Professional v 8.10 SP3 ()
STM 32 Cube IDE 1.6.1
Tutorials :
https://youtu.be/gL8OoS9E1rw
https://youtu.be/bX9m7KwA-8Y
https://youtu.be/rfBeq-Fu0hc
https://www.engineersgarage.com/accessing-ports-of-stm32-microcontroller/

## Slide 23: Circuit Diagram
PDF Link:
https://buetedu-my.sharepoint.com/:b:/g/personal/1606115_eee_buet_ac_bd/EZxj0MIKPdJOhWtbxd2vZdcBkjYmVESjbPqzSosBCdxEzw?e=cTpvTu

## Slide 24: Source Codes
#include "main.h"
#include <string.h>
#include <stdio.h>
#include<math.h>
ADC_HandleTypeDef hadc1;
UART_HandleTypeDef huart1;
void SystemClock_Config(void);
static void MX_GPIO_Init(void);
static void MX_ADC1_Init(void);
static void MX_USART1_UART_Init(void);
int main(void)
{
uint16_t raw;
uint16_t temp;
uint16_t x;
uint16_t a;
uint16_t b;
uint16_t c;
uint16_t voltage;
uint16_t i;
i = 0;
temp = 0;
char msg[10];
Descriptions:
Imports the necessary libraries
Declares System Clock, General Pupose Input Output Pins(GPIO), Analog to Digital Converter and Universal Synchronous/Asynchronous Receiver/Transmitter configuration functions
Initialize Variables:
  raw = value from adc
  temp = temporary variable
  x = average value over a period
  a = hundredth digit of voltage
  b = tenth digit of voltage
  c = unit digit of voltage
  voltage = the measured rms voltage
  i = counter variable
  msg = string for communication with tx,rx

## Slide 25: Source Codes
HAL_Init();
SystemClock_Config();
MX_GPIO_Init();
MX_ADC1_Init();
MX_USART1_UART_Init();
while (1)
{
HAL_ADC_Start(&hadc1);
HAL_ADC_PollForConversion(&hadc1, HAL_MAX_DELAY);
raw = HAL_ADC_GetValue(&hadc1);
temp = temp + raw;
i = i + 1;
if (i==10){
x = temp/10;
temp = 0;
i=0;
voltage = (x-1491)/5.6409 + 360;
sprintf(msg, "%hu\r\n", voltage);
HAL_UART_Transmit(&huart1, (uint8_t*)msg,strlen(msg), HAL_MAX_DELAY);
}
Descriptions:
Necessary peripherals are initialized
Raw voltage information is read through ADC using polling method
The raw values are averaged over a period
A linear relationship was established using two data points of raw data and voltage
Actual voltage is measured using the relationship
The value of the voltage is sent to virtual terminal for debugging

## Slide 26: Source Codes
a = floor(voltage/100);
b = floor(voltage/10);
b= b%10;
b = b<<4;
c = voltage%10;
c = c<<8;
GPIOB->ODR = a|b|c;
if (raw<60)
GPIOB->ODR = 0;
HAL_Delay(1);
if((voltage>466)||(raw<60))
{
HAL_GPIO_WritePin(GPIOA, GPIO_PIN_0, 0);
}
else
{
HAL_GPIO_WritePin(GPIOA, GPIO_PIN_0, 1);
}
}
}
Descriptions:
Since our three BCD 7 segment displays are connected with pins PB0-11, a 12-bit word is generated using four bits for each unit, tenth and hundredth digit
The 12-bit word is then sent to the Output Data Register of the Port B
If the measured voltage is greater than 6% of rated voltage of 440V for industrial usage, the load connecting relay is energized through mosfet
Otherwis the relay is de-enegized

## Slide 27: Source Codes
void SystemClock_Config(void)
{
RCC_OscInitTypeDef RCC_OscInitStruct = {0};
RCC_ClkInitTypeDef RCC_ClkInitStruct = {0};
RCC_PeriphCLKInitTypeDef PeriphClkInit = {0};
RCC_OscInitStruct.OscillatorType = RCC_OSCILLATORTYPE_HSE;
RCC_OscInitStruct.HSEState = RCC_HSE_ON;
RCC_OscInitStruct.PLL.PLLState = RCC_PLL_NONE;
if (HAL_RCC_OscConfig(&RCC_OscInitStruct) != HAL_OK)
{
Error_Handler();
}
RCC_ClkInitStruct.ClockType = RCC_CLOCKTYPE_HCLK|RCC_CLOCKTYPE_SYSCLK
|RCC_CLOCKTYPE_PCLK1|RCC_CLOCKTYPE_PCLK2;
RCC_ClkInitStruct.SYSCLKSource = RCC_SYSCLKSOURCE_HSE;
RCC_ClkInitStruct.AHBCLKDivider = RCC_SYSCLK_DIV1;
RCC_ClkInitStruct.APB1CLKDivider = RCC_HCLK_DIV1;
RCC_ClkInitStruct.APB2CLKDivider = RCC_HCLK_DIV1;
if (HAL_RCC_ClockConfig(&RCC_ClkInitStruct, FLASH_LATENCY_0) != HAL_OK)
{
Error_Handler();
}
PeriphClkInit.PeriphClockSelection = RCC_PERIPHCLK_ADC;
PeriphClkInit.AdcClockSelection = RCC_ADCPCLK2_DIV2;
if (HAL_RCCEx_PeriphCLKConfig(&PeriphClkInit) != HAL_OK)
{
Error_Handler();
}
}
Descriptions:
CubeIDE generated configuration code for Internal Clock

## Slide 28: Source Codes
static void MX_ADC1_Init(void)
{
hadc1.Instance = ADC1;
hadc1.Init.ScanConvMode = ADC_SCAN_DISABLE;
hadc1.Init.ContinuousConvMode = DISABLE;
hadc1.Init.DiscontinuousConvMode = DISABLE;
hadc1.Init.ExternalTrigConv = ADC_SOFTWARE_START;
hadc1.Init.DataAlign = ADC_DATAALIGN_RIGHT;
hadc1.Init.NbrOfConversion = 1;
if (HAL_ADC_Init(&hadc1) != HAL_OK)
{
Error_Handler();
}
/** Configure Regular Channel
*/
sConfig.Channel = ADC_CHANNEL_1;
sConfig.Rank = ADC_REGULAR_RANK_1;
sConfig.SamplingTime = ADC_SAMPLETIME_1CYCLE_5;
if (HAL_ADC_ConfigChannel(&hadc1, &sConfig) != HAL_OK)
{
Error_Handler();
}
}
Descriptions:
CubeIDE generated configuration code for ADC and USART
static void MX_USART1_UART_Init(void)​
{​
huart1.Instance = USART1;​
huart1.Init.BaudRate = 115200;​
huart1.Init.WordLength = UART_WORDLENGTH_8B;​
huart1.Init.StopBits = UART_STOPBITS_1;​
huart1.Init.Parity = UART_PARITY_NONE;​
huart1.Init.Mode = UART_MODE_TX_RX;​
huart1.Init.HwFlowCtl = UART_HWCONTROL_NONE;​
huart1.Init.OverSampling = UART_OVERSAMPLING_16;​
if (HAL_UART_Init(&huart1) != HAL_OK)​
{​
Error_Handler();​
}​
}​
​

## Slide 29: Source Codes
static void MX_GPIO_Init(void)
{
GPIO_InitTypeDef GPIO_InitStruct = {0};
/* GPIO Ports Clock Enable */
__HAL_RCC_GPIOD_CLK_ENABLE();
__HAL_RCC_GPIOA_CLK_ENABLE();
__HAL_RCC_GPIOB_CLK_ENABLE();
/*Configure GPIO pin Output Level */
HAL_GPIO_WritePin(GPIOA, GPIO_PIN_0, GPIO_PIN_RESET);
/*Configure GPIO pin Output Level */
HAL_GPIO_WritePin(GPIOB, GPIO_PIN_0|GPIO_PIN_1|GPIO_PIN_2|GPIO_PIN_10
|GPIO_PIN_11|GPIO_PIN_3|GPIO_PIN_4|GPIO_PIN_5
|GPIO_PIN_6|GPIO_PIN_7|GPIO_PIN_8|GPIO_PIN_9, GPIO_PIN_RESET);
Descriptions:
CubeIDE generated configuration code for GPIO
/*Configure GPIO pin : PA0 */
GPIO_InitStruct.Pin = GPIO_PIN_0;
GPIO_InitStruct.Mode = GPIO_MODE_OUTPUT_PP;
GPIO_InitStruct.Pull = GPIO_NOPULL;
GPIO_InitStruct.Speed = GPIO_SPEED_FREQ_LOW;
HAL_GPIO_Init(GPIOA, &GPIO_InitStruct);
/*Configure GPIO pins : PB0 PB1 PB2 PB3
PB4 PB5 PB6 */
GPIO_InitStruct.Pin = GPIO_PIN_0|GPIO_PIN_1|GPIO_PIN_2|GPIO_PIN_3
|GPIO_PIN_4|GPIO_PIN_5|GPIO_PIN_6;
GPIO_InitStruct.Mode = GPIO_MODE_OUTPUT_PP;
GPIO_InitStruct.Pull = GPIO_PULLDOWN;
GPIO_InitStruct.Speed = GPIO_SPEED_FREQ_LOW;
HAL_GPIO_Init(GPIOB, &GPIO_InitStruct);
/*Configure GPIO pins : PB10 PB11 PB7 PB8
PB9 */
GPIO_InitStruct.Pin = GPIO_PIN_10|GPIO_PIN_11|GPIO_PIN_7|GPIO_PIN_8
|GPIO_PIN_9;
GPIO_InitStruct.Mode = GPIO_MODE_OUTPUT_PP;
GPIO_InitStruct.Pull = GPIO_NOPULL;
GPIO_InitStruct.Speed = GPIO_SPEED_FREQ_LOW;
HAL_GPIO_Init(GPIOB, &GPIO_InitStruct);
}
}

## Slide 30: Difficulties
Live voltage change during simulation was not possible as there was no variable ac voltage source in the proteus library.
In this design the microcontroller is powered by an independent source as connecting the microcontroller with the main power supply line might cause damage during the time when there is overvoltage.